## Eitech Robo-Controller
Hardware: Atmel SAMW25 = Atmel SAMD21 ARM Cortex M0+ 32 Bit micro controller with WiFi module

- 4 motor ports M1 – M4 (3 of those adjustable in 256 steps), forward, back, coasting („sail“), brake, max. 1A per phase
- 1 port with MOSFET S1, max. 2A, adjustable in 256 steps
  7 general purpose IO pins J1 – J7 (five of those configurable as analog input or PWM output), can be used for servos, analog sensors or LEDs (max 30mA), 5V tolerant when configured as input
- I²C port for a maximum of 127 digital sensors (GPS, magnetometer…), actors or displays
- serial port (debugging, communication or to connect ultrasound distance sensors
- USB port can be used as serial port for debugging
- switch SW shares a pin with supply voltage measurement, can be polled in software
- regular IO pins use 1/10 inch standard to be compatible with DuPont and servo connectors
- JST socket on I²C port for Sensebox compatibility
- JST socket for power supply (7V to 14V) for compatibility with popular rechargebale LiPo batteries used for R/C models
- power can be alternatively supplied via USB (testing environment connected to PC, power bank), max. 600mA total current
- 2MBit flash memory for settings, web interface or data logging
- tinker with the board – you‘ll be able to connect eight servos and four motors
The operating voltage of the micro controller is 3.3V. Pins for sensors and servos use 5V. Motors and S1 are operated with input voltage. Since input ports are 5V tolerant, analog sensors can be used without having to connect additional voltage regulators.

The supplied documentation descibes usage of sensors available from Eitech, but also informs on readily available generic sensors.
### Software supplied with the board
The Robo Controller boards come pre-installed with a firmware that provides a simple web frontend to configure network settings and test functionality and wiring. This firmware also provides a REST API that allows to set motor speeds or read sensor values. The REST API is also used to communicate with the Eitech Robotics Android app.
### Eitech-App
The Eitech app will be available for Android mid February via Google Play store and a version for the iPhobe will foolow end of February. The app is currently prepared for three kits: The robot with caterpillar threads LED eyes and two servos, tower crane (C35) and three axle truck (C710). There is also the possibility to upgrade the robot with ultrasound distance sensor and two microswitches for collision detection to enable an autonomous mode (already part of the firmware).
### Programming using the Arduino IDE
The Arduino IDE is primarily targeted at an audience of 12 years or older. For compatibility and performance reasons Arduino is widely used in autonomic roboter leagues like Robo Cup and has a large user base at senior high schools, colleges and universities.

Eitech provides board support packages for Arduino 1.8 onwards. These are tested with Linux and Windows (MacOS is currently untested, but should work as well). Since the same micro controller core is used in Arduino Zero or Adafruit Feather M0, the majority of Arduino libraries is compatible with the Robo Controller. The board support package for Arduino is available instantly.

Code examples include, but are not limited to the web frontend for the remote control firmware and a simple automous robot that uses ultra sound sensors for distance measurement and micro switches for collision detection. The samples are extensively commented and kept short for good readability. Future sensors that are offered by Eitech will be accompagnied by code samples as of availability. Documentation for generic sensors can be found in the Arduino wiki.
### Programming using Microsoft Makecode/PXT
The graphical development environment Makecode/PXT addresses children of 8 years up. Makecode/PXT is the most commonly used development environment for BBC Microbit (Great Britain) and Calliope (Germany).

Programming using Makecode/PXT is done completely in the browser. The finished program is downloaded as UF2 file and copied to the Robo Controller that mimics a USB mass storage device. No local software installation is necessary!

With Makecode/PXT the program flow is clicked together from code blocks. Loops, repetitions or fork in the flow are visualized very well. Documentation written for Microbit or Calliope can be used in courses without the need for changes. Makecode/PXT is available instantly.

https://pxt.eitech-robotics.de/ → Choose „Eitech Robotics Winc1500“ and start over...
### REST API
The REST API allows to program in any language with sufficient support for HTTP requests and the parsing of JSON responses. This facilitates integration in projects where robotics might not be the primary subject. We provide examples for several languages, for exaple a wether statation that is completely implemented in HTML and JavaScript.
### Outlook on programming using Circuit Python
Should there be sufficient interest on programming the Robo Controller using the object oriented script language Python we will evaluate the possibility to fully port the Cirtuit Python interpreter to the Robo Controller. If you are interested in a preview build, contact us by email to receive a beta build of the Circuit Python interpreter.
### Open Source
At https://github.com/eitech-robotics/ you will find code samples for all supported languages and environments and the source code of the firmware upon delivery licensed as Open Source Software. Source codes are GPL licensed which allows for flexible usage and easy modification.