## Eitech Robo-Controller
Hardware: Atmel SAMW25 = Atmel SAMD21 ARM Cortex M0+ 32 Bit micro controller with WiFi module

- 4 motor ports M1 – M4 (3 of those adjustable in 256 steps), forward, back, coasting („sail“), brake, max. 1A per phase
- 1 port with MOSFET S1, max. 2A, adjustable in 256 steps
  7 general purpose IO pins J1 – J7 (five of those configurable as analog input or PWM output), can be used for servos, analog sensors or LEDs (max 30mA), 5V tolerant when configured as input
- I²C port for a maximum of 127 digital sensors (GPS, magnetometer…), actors or displays
- serial port (debugging, communication or to connect ultrasound distance sensors
- USB port can be used as serial port for debugging
- switch SW shares a pin with supply voltage measurement, can be polled in software
- regular IO pins use 1/10 inch standard to be compatible with DuPont and servo connectors
- JST socket on I²C port for Sensebox compatibility
- JST socket for power supply (7V to 14V) for compatibility with popular rechargebale LiPo batteries used for R/C models
- power can be alternatively supplied via USB (testing environment connected to PC, power bank), max. 600mA total current
- 2MB flash memory for settings, web interface or data logging
- tinker with the board – you‘ll be able to connect eight servos and four motors
The operating voltage of the micro controller is 3.3V. Pins for sensors and servos use 5V. Motors and S1 are operated with input voltage. Since input ports are 5V tolerant, analog sensors can be used without having to connect additional voltage regulators.

The supplied documentation descibes usage of sensors available from Eitech, but also informs on readily available generic sensors.
### Software supplied with the board
The Robo Controller boards come with a WiFi remote control software pre-installed. This software either provides a WiFi access point or can be configured as WiFi client. After connecting with a smart phone or tablet a touch enabled web interface can be used to control three servos, four motors and one switch. A button on the board can be used to switch WiFi modes.

The interface can be configured to suit the needs of different models: tracked vehicles (steered by velocity differences of left and right track), wheeled vehicles (servo for steering, motor for propulsion) oder sliders only for models like the crane.

As pre-installed the software is configured for two servos, four motors (three of those are continously adjustable) and one switch (mapped to different effects). If changes are needed, the user has full access to the source code (ope source and extensively commented). The source code can be edited, compiled and installed using Arduino IDE 1.8 onwards. To adjust only the web interface, JavaScript and HTML knowledge is sufficient.

No special software is needed to update the firmware: The Eitech Robo Controller mimics a USB thumb drive when connected to a PC. Just drag a UF2 file to the virtual drive. As soon as writing is done the controller reboots and installs this UF2 firmare. The WiFi web interface and various programs to test functionality are available as download from eitech.de.
### Programming using the Arduino IDE
The Arduino IDE is primarily targeted at an audience of 12 years or older. For compatibility and performance reasons Arduino is widely used in autonomic roboter leagues like Robo Cup and has a large user base at senior high schools, colleges and universities.

Eitech provides board support packages for Arduino 1.8 onwards. These are tested with Linux and Windows (MacOS is currently untested, but should work as well). Since the same micro controller core is used in Arduino Zero or Adafruit Feather M0, the majority of Arduino libraries is compatible with the Robo Controller. The board support package for Arduino is available instantly.

Code examples include, but are not limited to the web frontend for the remote control firmware and a simple automous robot that uses ultra sound sensors for distance measurement and micro switches for collision detection. The samples are extensively commented and kept short for good readability. Future sensors that are offered by Eitech will be accompagnied by code samples as of availability. Documentation for generic sensors can be found in the Arduino wiki.
### Programming using Microsoft Makecode/PXT
The graphical development environment Makecode/PXT addresses children of 8 years up. Makecode/PXT is the most commonly used development environment for BBC Microbit (Great Britain) and Calliope (Germany).

Programming using Makecode/PXT is done completely in the browser. The finished program is downloaded as UF2 file and copied to the Robo Controller that mimics a USB mass storage device. No local software installation is necessary!

With Makecode/PXT the program flow is clicked together from code blocks. Loops, repetitions or fork in the flow are visualized very well. Documentation written for Microbit or Calliope can be used in courses without the need for changes. Makecode/PXT can be tested immediately with minor limitations (choose Adafruit Feather M0 Express as target platform). Blocks for easier access to the motor drivers and easier reading of the ultrasound sensor are being prepared and will be available as the delivery of the Robo Controller starts.

Any sensor offered by Eitech will be accompagnied by programming examples . View the documentation for Microbit and Calliope to learn how to connect and use generic sensors.

https://maker.makecode.com/ → Choose Adafruit Feather M0 Express and start programming...
### Outlook on programming using Circuit Python
Should there be sufficient interest on programming the Robo Controller using the object oriented script language Python we will evaluate the possibility to fully port the Cirtuit Python interpreter to the Robo Controller. If you are interested in a preview build, contact us by email to receive a beta build of the Circuit Python interpreter.